## Slide 1: Lecture 3- Modeling Real-Time Systems
Deepak Gangadharan

## Slide 2: Modeling Real-Time System - Recap
Application/ Workload modeled as task graph
Resource Model
Scheduling and Resource Access control algorithms

## Slide 3: An Example – Inverted Pendulum
A model
Actual System
Source: http://www.st.ewi.tudelft.nl/mitra/teaching/rts/2019/files/lect02-online-scheduling.pdf
Model should be adequately expressive and tractable

## Slide 4: What is good modeling?
Source: http://www.st.ewi.tudelft.nl/mitra/teaching/rts/2019/files/lect02-online-scheduling.pdf
Intractability
Expressiveness
Good
Model
Far from
reality
Too
Complex
Read input
Compute
Write
output
Control task
Any details abstracted?
Alternate Model

## Slide 5: Application/Task Modeling

## Slide 6: Relationship between deadline and period
Implicit deadline: Deadline is equal to period
Constrained deadline: Deadline is less than or equal to period
Arbitrary deadline: Deadline can be smaller, equal or greater than period

## Slide 7: Periodic Task Model – Hyperperiod
Each computation or data transmission is modeled as a periodic task
Each periodic task is a sequence of jobs
Hyperperiod (H) – Time after which the release patterns of a periodic task set repeat
H = LCM() for
Task 1
Period = 8
Task 2
Period = 6
H = 24

## Slide 8: Precedence Constraints
Determines the order of execution of tasks/jobs
Precedence constraints specified using a partial-order relation <, called precedence relation over the job set
Job is a predecessor of job given by <
A job with predecessors is ready for execution at or after release time and after all the predecessors have completed execution
Represented using a directed graph
Each vertex is a job in
Called a precedence graph

## Slide 9: Task Graph
A general way to represent an application
Vertices represent jobs and edges represent dependencies among jobs
If all edges are precedence edges, then the graph is a precedence graph
The numbers in brackets above each job give the release time and absolute deadline
A task graph can contain different types of edges representing different types of dependencies
Independent jobs with
period = 2 and relative deadline = 7
Dependent jobs with
period = 3 and relative deadline = 3

## Slide 10: Types of Dependencies
Data dependency – Not captured by precedence graph because data dependent tasks need not execute in any particular order
  Parameter of edge from to is the volume of data shared or sent
Temporal Dependency – Some jobs may have constraints on the temporal distance (difference in completion times) between them
AND/OR Precedence
  All the immediate predecessors must finish completion before the job can start execution – called AND jobs
  OR jobs can start execution at or after release time and once one or some of its predecessors have completed
Conditional Branches – Conditional execution of branches
  Consists of branch jobs and join jobs

## Slide 11: Resource Modeling

## Slide 12: Resource Graph
Provides configuration of resources
Each vertex represents a processor or another resource
Attributes of the vertex – parameters of the resource such as resource type, number of available units, etc.
Two types of edges in resource graph
  is-a-part-of edge : This edge from vertex to vertex means that is a component of
  accessibility edges : Connectivity between components

## Slide 13: Scheduling and Resource Access Control

## Slide 14: Scheduling
Jobs scheduled using scheduling algorithms
Jobs allocated resources using resource access-control protocols
Scheduler implements both the above algorithms
Scheduler assigns jobs to processors or other resources
Schedule: Assignment of jobs in the system on the available processors
Valid schedules:
  Every processor is assigned to at most one job at any time
  Every job is assigned at most one processor at any time
  A job is scheduled only after release time
  As per scheduling algorithm, the total amount of processor time assigned to a job is its maximum or actual execution time
  Satisfies all the precedence and resource usage constraints

## Slide 15: Feasibility and Optimality
A valid schedule is a feasible schedule if every job is finished by deadline or meets its timing constraints
Schedulability: A set of jobs is schedulable according to a scheduling algorithm if it always produces a feasible schedule
Optimality of a Scheduler: A scheduling algorithm is optimal if it always produces a feasible schedule of the jobs if there exists a feasible schedule
Scheduler may work on performance measures such as tardiness, lateness, response time, and miss, loss and invalid rates.

## Slide 16
Questions?