## Slide 1: Lecture 23: Multiprocessor Scheduling
Deepak Gangadharan (Taken from slides by Dr. Mitra Nasri from TU Delft) Link: http://www.st.ewi.tudelft.nl/mitra/teaching/rts/2019/

## Slide 2: Future real-time systems – Need lot of computational power

## Slide 3: Switching to multicore systems
How to exploit multicores in real-time systems?
Industrial trend 1: By consolidation
  Port the existing functionalities of a multiple processors into a multicore platform
    Example: ECU consolidation in automotive industry
    Reduces hardware cost and communication delays
Industrial trend 2: By parallel programming techniques
  By parallelizing the application code, each code segment can run on a different core in parallel  tasks will have a shorter response time
  Main challenges:
    How to split the code into parallel segments that can be executed simultaneously
    How to allocate such segments to different cores
    How to analyse the WCET of the applications on a multicore platform

## Slide 4: Industry’s Challenges
Problem 1: Parallelizing legacy code implies a tremendous cost and effort due to:
  Redesigning the application
  Rewriting the source code
  Updating the operating system
  Writing new documentation
  Testing the system
  Software certification
Problem 2: Execution of tasks on a multicore platform causes a lot of conflicts/interferences on hardware and software resources
  Multiple tasks (running on multiple cores) may want to access the memory at the same time
  Tasks may evict each other’s cache blocks in the shared caches
  WCET of a task will depend on the set of co-running tasks on the platform

## Slide 5: WCET in multicore
Test by Lockheed Martin Space
Systems on 8-core platform

## Slide 6: Cache in multicore systems
Possible Solution: partition the
last-level cache between tasks
Issue: Reducing cache size of a task will increase its WCET and hence the task’s utilization

## Slide 7: Cache in multicore systems
Possible Solution: partition the
last-level cache between tasks
Issue: Reducing cache size of a task will increase its WCET
Two possible approaches are
Use “non-preemptive scheduling” on the cores (to avoid cache conflicts on L1 and L2)
Partition the shared cache L3 by the number of cores (and not number of tasks which is usually much larger

## Slide 8: Memory Banks
To reduce memory conflicts, DRAM is divided into banks

## Slide 9: Main memory and I/O conflicts
When cores concurrently access main memory, DRAM accesses have to be queued, causing slowdown
A similar problem occurs when tasks running in
different cores request to access I/O devices at the
same time

## Slide 10: How bad memory conflict can be?
Test on Intel Xeon

## Slide 11: Types of multicore systems
Identical cores ARM’s MPCore
Heterogeneous cores STI’s Cell Processor

## Slide 12: Example: ARM Big.LITTLE architecture
There are many open scheduling problems in heterogeneous platforms: we will focus on identical cores

## Slide 13: Task Models for Parallel Real-Time Tasks
Representing a parallel code requires more complex structures like a graph (usually a directed acyclic graph or DAG)

## Slide 14: Structured Parallelism
Fork-Join Graphs (a special type of DAG)
  After a fork node, all immediate successors must be executed in any order
  A join node is executed only after all immediate predecessors are completed
Nested fork-join model can have nested forks and joins

## Slide 15: Important Factors

## Slide 16: Multiprocessor Models

## Slide 17
Questions?