## Slide 1: Lecture 2- Modeling Real-Time Systems
Deepak Gangadharan

## Slide 2: Recap - Digital Controller
Reference input, Sensor measurements are typically analog
Controller performs A/D conversion, applies a control law and performs computation and D/A conversion of the control output
The analog control output controls the actuator, which in turn changes the state of the plant
Periodic Digital
Controller

## Slide 3: What will we learn?
What influences the response time of a system (or its tasks)
How can we evaluate or analyze the response time?
How can we design a time-predictable system?

## Slide 4: Motivation – Why modeling is important?
Multiple Sensors
Multiple
Tasks
Various periods of activation
Event based activation
Shared data

## Slide 5: Preliminary Notions
What is a Task?
  a piece of code that implements a system functionality
  can have multiple inputs and outputs
  can be activated by events (e.g., user command or an interrupt) or by time (e.g., by periodic timer interrupt)
Tasks can usually share data, communicate with each other and perform i/o operations.

## Slide 6: Preliminary Notions
Job
  An instance of a task that has arrived at the system
Task 2
Task 1
…
…

## Slide 7: Preliminary Notions
Execution Time – Denoted by for task
  Time required on the processor for running a task to completion
Actual execution times may vary for each instance of task execution
Typically is taken as either worst-case execution time (for hard real-time systems) or average case execution time (for soft real-time systems)
Task 1
…

## Slide 8: Preliminary Notions
Deadline – Denoted by for task
  Instant of time before which the task execution must finish
Relative deadline – It is calculated relative to the release time.
Absolute deadline = Release time + Relative deadline
Task 1
…
Relative
deadline
10
90
Relative deadline = 80
Absolute deadline = 90

## Slide 9: Modeling Real-Time System
Application/ Workload modeled as task graph
Resource Model
Scheduling and Resource Access control algorithms

## Slide 10
Application/Task Model

## Slide 11: Activation Pattern of Tasks
Periodic
  Single rate (all tasks have same period)
  Multi rate (tasks have different periods)
Aperiodic
  Bounded arrival time (sporadic)
  Unbounded arrival time (event based activation)
Aperiodic
task
Periodic
task
…
…

## Slide 12: Periodic
Each task/group of tasks executes/execute repeatedly with a particular period
Allows static analysis techniques
Widely used in real-time systems

## Slide 13: Aperiodic
Activated by events
Workload is dynamic (cannot be predicted)

## Slide 14: Sporadic
Task whose next activation time is lower bounded by a value called minimum inter arrival time (also called period)

## Slide 15
Questions?